  1. A Q Q-1 M Operation
    000000000	001101011	0	010110110	Data
    101001010	001101011	0	010110110	A = A - M
    110100101	000110101	1	010110110	Shift
    111010010	100011010	1	010110110	Shift
    010001000	100011010	1	010110110	A = A + M
    001000100	010001101	0	010110110	Shift
    110001110	010001101	0	010110110	A = A - M
    111000111	001000110	1	010110110	Shift
    001111101	001000110	1	010110110	A = A + M
    000111110	100100011	0	010110110	Shift
    110001000	100100011	0	010110110	A = A - M
    111000100	010010001	1	010110110	Shift
    111100010	001001000	1	010110110	Shift
    010011000	001001000	1	010110110	A = A + M
    001001100	000100100	0	010110110	Shift
    000100110	000010010	0	010110110	Shift
  2. mulh x10, x11, x12 // Upper 64 bits stored in x10 00000010110001011001010100110011
    mul x10, x11, x12 // Lower 64 bits stored in x10
    00000010110001011000010100110011
  1. Fig. 1 seems to be an implementation of booth’s algorithm, solve using the same process as problem 1. D6 = 1101 0110, 7C = 1111 1000
A	Q	Q-1	M	Operation
000000000	001111100	0	011010110	Data
000000000	000111110	0	011010110	Shift
000000000	000011111	0	011010110	Shift
100101010	000011111	0	011010110	A = A - M
110010101	000001111	1	011010110	Shift
111001010	100000111	1	011010110	Shift
111100101	010000011	1	011010110	Shift
111110010	101000001	1	011010110	Shift
111111001	010100000	1	011010110	Shift
011001111	010100000	1	011010110	A = A + M
001100111	101010000	0	011010110	Shift
000110011	110101000	0	011010110	Shift

  For Fig 2:
  The algorithm is:
  1. Look for the last digit of the product.
  2. If Zero then
    a) Shift product right
  3. Otherwise
    a) add multiplicand to the left 8 bits of the product
    b) shift product right 1 bit
B0 = 0, Product = 00000000 00000000 -> Shift right -> 00000000 00000000
- B1 = 0, Product = 00000000 00000000 -> Shift right -> 00000000 00000000
- B2 = 1, Product = 00000000 00000000 -> Add A to high byte -> 11010110 00000000 -> Shift right -> 01101011 00000000
- B3 = 1, Product = 01101011 00000000 -> Add A to high byte -> 01101011 00000000 + 11010110 00000000 = (1)01000001 00000000 -> Shift right (carry) -> 10100000 10000000
- B4 = 1, Product = 10100000 10000000 -> Add A to high byte -> 10100000 10000000 + 11010110 00000000 = (1)01110110 10000000 -> Shift right (carry) -> 10111011 01000000
- B5 = 1, Product = 10111011 01000000 -> Add A to high byte -> 10111011 01000000 + 11010110 00000000 = (1)10010001 01000000 -> Shift right (carry) -> 11001000 10100000
- B6 = 1, Product = 11001000 10100000 -> Add A to high byte -> 11001000 10100000 + 11010110 00000000 = (1)10011110 10100000 -> Shift right (carry) -> 11001111 01010000
- B7 = 0, Product = 11001111 01010000 -> Shift right -> 01100111 10101000
- 01100111 10101000 = 67A8
  1. mul x10, x11, x12
    00000010110001011000010100110011
  2. For fig. 1: 11 * 2ns = 22 ns
    For fig. 2: 14 * 2ns = 28 ns
R	Q	D	Operation
0000	1110	0101	Data
0000	0111	0101	Shift right
0001	1100	0101	Shift left
0011	1000	0101	Shift left
0111	0000	0101	Shift left
0010	0000	0101	R - D
0100	0001	0101	Shift right
0010	0001	0101	Shift left

  1. For refined multiplication you would perform 8 additions and up to 7 shifts. Booth’s algorithm will take less cycles and less latency as a result, it should be around half the latency.
    For unsigned the refinement might not require any adjustments because the refined version is designed for unsigned integers.
    For signed integers, you need to consider two's complement. The hardware would need to be able to handle negative values, which might include an additional step change the product's sign.
Step	Multiplier	Current Bit	Multiplicand	Product	Accumulation Register
1	0010 0111 (LSB)	1	1001 1100 (Shifted 0)	1001 1100	1001 1100
2	0010 0110	1	1001 1100 (Shifted 1 left)	1 0011 1000	10 0110 0100
3	0010 0100	1	1001 1100 (Shifted 2 left)	100 1110 00	1011 1010 00
4	0010 0000	0	-	0	-
5	0000 0000	1	1001 1100 (Shifted 4 left)	1001 1100 0000	1 0111 1100 0100

Step	Action	Divisor	Dividend	Quotient (Q)	Remainder (R)	Comment
0	Initial	0010 0111	1001 1100	0000	1001 1100	Initial state
1	Subtract divisor from dividend	0010 0111	1001 1100	0001	0111 0101	1 subtraction possible, Q = 1, R = dividend - divisor
2	Subtract divisor from remainder	0010 0111	0111 0101	0010	0100 0010	Another subtraction, Q = 2, update R
3	Subtract divisor from remainder	0010 0111	0100 0010	0011	0000 1111	Another subtraction, Q = 3, update R
4	Subtract divisor from remainder	0010 0111	0000 1111	0100	(Negative)	Cannot subtract without going negative, stop here

Carry into MSB⊕Carry out of MSB
Carry into MSB (Most Significant Bit): This carry is part of the calculation within the bounds of the number.
Carry out of MSB: It would be used for a bit beyond the bounds of the number.
If both MSB are 0, this means that the output must be 0 as two 0s is equivalent to adding two positive numbers, if we get a 1 out of the XOR, this means that we got a negative number which is impossible without an overflow.
If both MSB are 1 but the result is a 1 from the XOR, this means that we added two neg. numbers and got a positive from an overflow.